## Slide 1: XNOR-Net and Binary Connect Hardware Design
Lucas B., Bibrak C., Adam D., Prateek S.
E501 Design Project Presentation
4/16/2018

## Slide 2: Introduction
Hardware designs were created to implement the basic hardware building blocks of the following papers:
  “XNOR-Net: ImageNet Classification Using Binary Convolutional Neural Networks”
  “BinaryConnect: Training Deep Neural Networks with binary weights during propagations”

## Slide 3: Feed-forward network using a trained neural network model
For the current scope of the project, we consider MNIST dataset which consists of 10 classes of images i.e. 0 to 9.
Once the training of the neural network is done using any machine, our hardware design focuses on achieving speedup in the classification phase.
The weights learned by the neural network will be inserted in the module using a BRAM to the feed forward network.
These weights along with the images to be classified would be used as an input to the feed forward network on an FPGA.
The scope of our project is only defined for the implementation of the fully connected layer after the convolutions have been done.

## Slide 4
0
3
1
2
4
7
5
6
9
8
Input Image Size
28x28
20x24x24
Kernel Size : 5x5
20 Different Kernels
20 Images
20x12x12
Kernel Size : 2x2
20 Different Kernels
Maxpooling
50x8x8
Kernel Size : 5x5
50 Different Kernels
50 Images
50x4x4
Kernel Size : 2x2
50 Different Kernels
Maxpooling
Vector Size: 800
Vector Size: 500
Vector Size: 10
Fully Connected Layer
Convolution Layer 1
Convolution Layer 2

## Slide 5: Fully Connected Layer
Input Layer becomes a vector, the weights which are multiplied and accumulated become a matrix. This whole process of Matrix and Vector multiplication along with accumulation is simply a Matrix-Vector Multiplication.
Input Vector (I) : 800 x 1
Weight Matrix (W1) : 500 x 800
Hidden Layer (H) : H = W1 x I = [500 x 800] [800 x 1] = [500 x 1]
Weight Matrix (W2) : 10 x 500
Output Layer (O) : O = W2 x H = [10 x 500] [500 x 1] = [10 x 1]
This output layer which is a vector of 10 values classifies all the images in the possible 10 numbers according to MNIST Data Set we use.

## Slide 6
XNOR+POPCOUNT
Scalar Multiplication (alpha Normalization)
RAM
(BRAM on FPGA)
Multiplexor
[8x8 matrix] Wi (binary)
[8x1 vector] Vi (32-bit fixed point)
[8x1 vector] (32-bit fixed point)​
[8x1 vector] (16-bit fixed point)​
[8x1 vector] (16-bit fixed point)​
alphai (signed 16-bit fixed)
Normalizer​
[8x1 vector] (binary)
Scalar Multiplication (alpha Normalization)
Controller (FSM to control RAM and mux)
Control signals
XNOR-Net
Betai (signed 16-bit fixed)
(from Normalizer)
[8x1 vector] (32-bit fixed point)​

## Slide 7
Accumulator
Scalar Multiplication (alpha Normalization)
RAM
(BRAM on FPGA)
Multiplexor
[8x8 matrix] Wi (binary)
Vi = [8x1 vector] (32-bit fixed point)
[8x1 vector] (16-bit fixed point)​
[8x1 vector] (16-bit fixed point)​
[8x1 vector] (32-bit fixed point)​
alphai (32-bit fixed point)
Controller (FSM to control RAM and mux)
Address/Control signals
Control signals
Binary Connect

## Slide 8
XNOR-Net Core Components | Binary Connect Core Components
XNOR + Popcount Design Concept Performs multiplication and accumulation(MAC) operation optimizations. | Accumulator Performs multiplication and accumulation(MAC) operation optimizations.
Alpha and Beta Multipliers Performs multiplication of vector to scalar | Alpha Multiplier Performs multiplication of vector to scalar

## Slide 9: Modules

## Slide 10: Popcount Design Concept 1 (Slow)
Purely ripple carry adder (RCA) combination
RCA [31:30]
RCA [29:28]
RCA
RCA [3:2]
…
…
RCA
RCA [1:0]
8bit RCA
…
…
input
8bit RCA
8bit RCA
(sub)
Numbits = 32
Also, If you simply count the number of ones in a string, you need to apply:
  POPCOUNT = (NUMBER OF ONES) * 2 – (NUMBER OF BITS)

## Slide 11: Popcount Design Concept 2 (Better)
8 of 4-bit Lookups + ripple carry adder (RCA) combination
Look up table saves adders and reduces propagation time
4 bit lookup [31:28]
Input [3:0] | Popcount
0000 | 0
0001 | 1
0010 | 1
0011 | 2
0100 | 1
0101 | 2
0110 | 2
0111 | 3
1000 | 1
1001 | 2
1010 | 2
1011 | 3
1100 | 2
1101 | 3
1110 | 3
1111 | 4
4 bit lookup [27:24]
5bit RCA
4 bit lookup [7:4]
…
…
5 bit RCA
4 bit lookup [3:0]
8bit RCA
…
…
4 bit lookup table
input
8bit RCA
8bit RCA
(sub)
Numbits = 32
Still, you simply count the number of ones in a string, you need to apply:
  POPCOUNT = (NUMBER OF ONES) * 2 – (NUMBER OF BITS)

## Slide 12: Popcount Design Concept 3 (Best)
8 of 4-bit Lookups + ripple carry adder (RCA) combination
4 bit lookup [31:28]
Input [3:0] | Popcount
0000 | -4
0001 | -2
0010 | -2
0011 | 0
0100 | -2
0101 | 0
0110 | 0
0111 | 2
1000 | -2
1001 | 0
1010 | 0
1011 | 2
1100 | 0
1101 | 2
1110 | 2
1111 | 4
4 bit lookup [27:24]
5bit RCA
4 bit lookup [7:4]
…
…
5 bit RCA
4 bit lookup [3:0]
8bit RCA
…
…
4 bit lookup
input
8-bit popcount
Building the negative popcount values into LUT:
  Saves 2 RCA components

## Slide 13: 8-bit Popcount Design
8-bit Style | # RCA | # LUT4 | Speed | Area
Just RCA | 9 | 0 | slow | large
RCA+LUT | 3 | 2 | fast | med
RCA+LUT opt | 1 | 2 | fast | small

## Slide 14: XNOR and Popcount Results

## Slide 15: Scalar Multipliers
Multiplies a fixed point scalar value to an integer

## Slide 16: Scalar Multipliers
Multiplies a fixed point scalar value to a fixed point

## Slide 17: Accumulator
This module is the core of Binary Connect.
Multiplying the fixed point numbers to the binary weight matrix essentially is not multiplication. It is addition or subtraction depending on the corresponding weight in the weight matrix. For example, a three dimensional binary weight matrix and an input vector when multiplied behaves as follows:
Accumulator thus, removes the multiplication and replaces it with addition and subtraction operations.
As the accumulator is cheaper than the multiplier, its usage in the neural network design grants speedup.

## Slide 18: Block Diagram for accumulator
Adder/Subtractor
w0z
nn_in(0)
Weights(0)(0)
w0s0
Adder/Subtractor
nn_in(1)
Weights(0)(1)
w0s1
w0s6
Adder/Subtractor
nn_in(7)
c
w0s7
Weights(0)(7)
Adder/Subtractor
w0z
nn_in(0)
Weights(1)(0)
w1s0
Adder/Subtractor
nn_in(1)
Weights(1)(1)
w1s1
w1s6
Adder/Subtractor
nn_in(7)
c
w1s7
Weights(1)(7)

## Slide 19: Computation mechanism
The following matrix multiplication(but for 8x1 vector) is computed in the following manner:

## Slide 20
Schematic

## Slide 21
Waveform

## Slide 22: Scalar multiplier
Implementation of a 32-bit fixed-point multiplication
  16-bit inputs: 1-bit signal, 7-bit integer, 8-bit fraction
To perform fixed-point multiplication
  Consider inputs as two-complements and do 'normal' multiplication, then determine where the "point" is.
Source: https://www.allaboutcircuits.com/technical-articles/multiplication-examples-using-the-fixed-point-representation/

## Slide 23: Xilinx 7 Series FPGA

## Slide 24: Xilinx 7 Series FPGA
Configurable Logic Block
  Combinatorial functions
  Flip-Flops
Slices
  Four six-input LUTs
  Multiplexers
  Carry Chains
  Four Flip-Flops/Latches (plus another 4)

## Slide 25: Xilinx 7 Series FPGA
Source: Xilinx
Remarks: 3-stage pipeline

## Slide 26: Scalar Multiplier
Besides VHDL version, we designed two more implementations to study resource allocations.
  Verilog – small latency/area intensive
  Verilog - DSP

## Slide 27: Verilog: Area intensive vs DSP
Area:
DSP
Note: I indexes bits in 16-bit value
Note: I index 16-bit value in vector

## Slide 28: Verilog: Area intensive vs DSP
Area:
DSP
Slice Logic Utilization:
Number of Slice LUTs: 3288 out of 63400 5%
Number used as Logic: 3288 out of 63400 5%
Slice Logic Distribution:
Number of LUT Flip Flop pairs used: 3288
Number with an unused Flip Flop: 3288 out of 3288 100%
Number with an unused LUT: 0 out of 3288 0%
Number of fully used LUT-FF pairs: 0 out of 3288 0%
Multiplexers : 968
1-bit 2-to-1 multiplexer : 968
DSP
Number of DSP48E1s: 0 out of 240 0%
Slice Logic Distribution:
Number of LUT Flip Flop pairs used: 0
Number with an unused Flip Flop: 0 out of 0
Number with an unused LUT: 0 out of 0
Multiplexers = : 0
1-bit 2-to-1 multiplexer : 0
DSP
Number of DSP48E1s: 24 out of 240 10%

## Slide 29: Results

## Slide 30: XNOR-NET Results

## Slide 31: Python Verification of XNOR-Net

## Slide 32
Binary Connect Results

## Slide 33
Python Verification of Binary Connect